## Slide 1: Computer Organization & Design
Dr Noor Mahammad Sk

## Slide 2: Grading Policy
Internal – 40% Weightage
  Quiz I - 20% Weightage
  Quiz II - 20% Weightage
External – 60% Weightage
  End Semester Exam – 40% weightage
  Project/Assignment – 20% Weightage
Copying and Malpractice will result in Zero Marks

## Slide 3: Outline
Introduction
Organization of Computer
Architectures
Representation of Instructions
Computer Arithmetic
Processing unit and Processor Design
Memory unit & Memory Organization
IO Unit & IO Systems
Pipelined Processors

## Slide 4: Digital Computer/ Simply Computer
Computer: a fast calculating machine
  Accepts digitized input information
  Process it according to a list of internally stored instructions
  Produces the resulting output information
The list of instructions are called computer program
Internal storage is computer Memory

## Slide 5: Computer Types
Differs on
  Size
  Cost
  Computational Power
  Intended Use
Desktops
Portable Notebook
Workstations
  Engineering and Scientific applications

## Slide 6: Computer Types
Enterprise System (Mainframes)
  Used for business data processing
Servers
  Education, business and personal user communities
Super Computers
  Large scale numerical calculations
  Applications like:
    Weather forecasting
    Aircraft design and simulation

## Slide 7: Functional Units
INPUT
OUTPUT
I/O Unit
MEMORY
Processor Unit
ALU
CONTROL
Basic Functional Units of a Computer

## Slide 8: Input Unit
Accepts coded information through input units
Input devices
  Keyboard
  Joysticks
  Track balls
  Mouse
  Microphone

## Slide 9: Memory Unit
Stores programs and data
Two types
  Primary
  Secondary
Primary Memory
  Fast and operates at electronic speeds
  Programs must be stored in the memory while they are being executed
  Large number of semiconductor storage cells

## Slide 10: Terminology
Random Access Memory
  any location in the memory can be reached in a short and fixed amount of time after specifying its address.
Access time is fixed, independent of the location of the word being accessed.
It typically ranges from few ns to 100ns
Memory access time
  Time required to access one word

## Slide 11: Primary Memory
Memory of a computer implemented as a memory hierarchy or 3 or 4 levels of semiconductor RAM units with different speeds and sizes.
The small, fast RAM units called caches
The largest & slowest unit is referred as the main memory
Primary storage is essential, it tend to be expensive with increase of size.

## Slide 12: Secondary Memory
When large amounts of data and many programs have to be stored
Particularly for information that is accessed infrequently.
Secondary storage devices
  Magnetic disks & tapes
  Optical disks (CD-ROMs)
  Flash memory devices

## Slide 13: Arithmetic Logic Unit (ALU)
Most computer operations are executed in the ALU of the processor
Suppose: two numbers located in the memory are to be added
  They brought into the processor and the actual addition is carried out by the ALU
  The sum may then be stored in the memory or retained in the processor for immediate use
  Control and ALU are many times faster than other devices connected to the device

## Slide 14: Output Unit
Counterpart of the input unit
To send processed results to the outside world
Printers
Graphics display
Audio output devices (Speakers)

## Slide 15: Control Unit
The operations of following units must be coordinated in some way
  Memory
  Arithmetic and logic unit
  Input and output units stores and process information and performs I/O operations
Control unit is effectively the nerve center that sends control signals to other units and sends their states.
Much of the control circuitry is physically distributed throughout the machine

## Slide 16: Summary
The computer accepts information in the form of programs and data through an input unit and stores it in the memory
Information stored in the memory fetched, under program control, into an ALU, where it is processed
Processed information leaves the computer through an output unit
All activities inside the machine are directed by the control unit.

## Slide 17: Basic Operational Concepts
To perform a given task, an appropriate program consisting of a list of instructions is stored in the memory.
Individual instructions are brought from the memory into the processor
Processor executes the specified operations
Data to be used as operands are also stored in the memory

## Slide 18: Basic Operational Concepts
Add LOCA, R0
R0  operand in LOCA + R0
Original contents of the LOCA are preserved
Where as those of R0 are overwritten
This instruction require performance of several steps:
  Instruction is fetched from memory into the processor
  The operand at LOCA is fetched
  Add operand of LOCA and operand of R0
  Finally, the resulting sum is stored in register R0

## Slide 19: Basic Operational Concepts
In most of Modern computers the above instructions can be realized as follows for performance reasons (RISC or Load store)
  Load LOCA, R1
  Add R1, R0
Execution procedure
  First instruction transfers the contents of memory location LOCA into processor register R1
  Second instruction adds the content of R1 and R0 and places the sum into R0
  Note: This destroys the former contents of register R1 as well as those of R0, where the original contents of memory location LOCA are preserved.

## Slide 20: Basic Operational Concepts
Memory
MAR
PC
IR
MDR
R0
R1
.
.
Rn-1
Control
ALU
n general purpose
registers
Processor
Connections between the processors and the memory

## Slide 21: Processor
In addition to ALU and Control Circuitry
Number of registers
  Used for several different purposes
The Instruction Register (IR):
  Holds the instruction that is currently being executed
  Its output is available to the control circuits
    Generates the timing signals that control the various processing elements involved in executing the instruction

## Slide 22: Processor
Program Controller (PC) is specialized register
  Keep track of the execution of a program
  It contains memory address of the next instruction to be fetched and executed
  During the execution of an instruction, the contents of the PC are updated to correspond to the address of the next instruction to be executed
  PC points to the next instruction that is to be fetched from memory.

## Slide 23: Processor
n – general purpose registers R0 through Rn-1
Two registers facilitates communication with the memory
  Memory Address Register (MAR)
    holds the address of the location to be accessed
  Memory Data Register (MDR)
    Contains the data to be written into or read out of the addressed location

## Slide 24: Processor – Typical operational Steps
Program reside in the memory usually get there through the input unit
Execution of the program starts when PC is set to point to the first instruction of the program
The content of the PC are transferred to MAR
A read control signal is sent to the memory
The addressed word is read out of the memory and loaded into the MDR
Next, the contents of the MDR are transferred to the IR
At this point the instruction is ready to be decoded and executed

## Slide 25: Processor – Typical operational steps (If it uses ALU)
It is necessary to obtain the required operands
If an operand resides in the memory, it has to be fetched by sending its address to the MAR and initiate read cycle
Operand is read from the memory to MDR, then it is transferred from MDR to ALU
After one or more operands are fetched in this way, the ALU can perform the desired operation.
If the results of this operation is to be stored in the memory, the results is sent to MDR
The address of the location where the result is to be stored is sent to the MAR, and write cycle is initiated.

## Slide 26: Bus Structures
To achieve a reasonable speed of operation
  A computer must be organized so that all its units can handle one full word of data at a given time
When a word of data is transferred between units, all its bits are transferred in parallel,
  Bits are transferred simultaneously over many wires or lines, one bit per line.
A group of lines that serves as a connecting path for several devices is called a bus.
Buses: Data, Address and Control

## Slide 27: Bus Structure
Only one data transfer at a time
Only two units can actively use the bus at any given time.
Bus control lines are used to arbitrate multiple request for use of the bus.
Input
Output
Memory
Processor
Single Bus Structure

## Slide 28: Bus Structure
The main virtue of single bus structure
  Low cost
  Flexibility for attaching peripheral devices
Multiple buses achieve more concurrency in operations
  By allowing two or more transfers to be carried out at the same time
  Leads better performance
  With a penalty of increased cost
Slower devices on the bus uses buffers registers
  Keyboards, printers, magnetic and optical disks

## Slide 29: Bus Structure
Buffer registers smooth out timing differences among processors, memories, and I/O devices.
Buffers prevents a high speed processor from being locked to a slow I/O device during a sequence of data transfers.
This allows processors to switch rapidly from one device to another

## Slide 30: Software
System software is responsible for coordination of all activities in a computing system
Systems software is a collection of programs that are executed as needed to perform functions such as
  Receiving and interrupting user commands
  Entering and editing application programs and storing them as files in secondary storage devices
  Managing the storage and retrieval of files in secondary storage devices

## Slide 31: Software
System Software
  Running standard application programs such as word processors, spreadsheets, or games, with data supplied by the user
  Controlling I/O units to receive input information and produce output results
  Translating programs from source form prepared by the user into object form consisting of machine instructions
  Linking and running user-written application programs with existing standard library routines, such as numerical computation packages

## Slide 32: Software
Application programs are usually written in a high level programming language as
  C, C++, Java or Fortran
    Programmer specifies mathematical or text processing operations
These operations are described independent of the particular computer
A programmer using high level language need not know the details of machine program instructions
A system program called COMPILER translates the high level language program into a suitable machine language programs containing instructions

## Slide 33: Software – Operating System
This is a large program
Actually collection of routines, that is used to control the sharing of and interaction among various computer units as they execute application programs
OS routines perform the tasks required to assign computer resources to individual application programs.
These tasks includes
  assigning memory and magnetic disk space to program and data files
  Moving data between memory and disk units
  Handling I/O operations

## Slide 34: User Program and OS routine sharing of the Processor
Program
OS routines
Disk
Printer
t0
t1
t2
t3
t4
t5

## Slide 35: User Program and OS routine sharing of the Processor
t0 to t1- OS routine initiates loading the application program from disk to memory
Waits until the transfer is completed and then process the execution control to the application program
Similar activity occurs during the period of t2 to t3 and period t4 to t5
When the OS transfers the data file from the disk and prints the results
At t5 the OS may load and execute another application program.

## Slide 36: Software
Computer resources can be used more efficiently if several application programs are to be processed
Notice that the disk and the processor are idle during most of the time period t4 to t5
The operating system can load the next program to be executed into the memory from the disk while the printer is operating
Similarly, during t0 to t1, the OS can arrange to print the previous program’s results while the current program is being loaded from the disk

## Slide 37: Software
Thus OS manages the concurrent execution of several application programs to make the best possible use of computer resources
This pattern of concurrent execution is called multiprogramming or multitasking

## Slide 38: Performance
How quickly it can execute programs
Performance affected by
  Design of its hardware
  Its machine language instructions
  Compiler that translates the high level language programs in to machine language
For best performance, it is necessary to design the compiler, the instruction set, and the hardware in a coordinated way
We concentrate on the design of instruction set and hardware

## Slide 39: Performance
The processor time depends on the hardware involved in the execution of individual machine instructions
The hardware comprises of processor and memory which are usually connected by bus
Main
Memory
Cache
Memory
Processor
Bus

## Slide 40: Performance
At the start of execution
All program instructions and the required data are stored in the main memory
As execution proceeds
The instructions are fetched one by one over the bus into the processor, and the copy is placed in the cache
When the execution of an instruction calls for data located in the main memory, the data are fetched and a copy is placed in the cache
Later, if the same instruction or data item is needed a second time, it is read directly from the cache

## Slide 41: Processor Clock
Processor signal is controlled by a timing signal called a clock
The clock defines regular time intervals called clock cycles
To execute a machine instruction, the processor divides the action to be performed into a sequence of basic steps, such that each step can be completed in one clock cycle
The length P of one clock cycle is an important parameter that affects processor performance
Clock rate R = 1/ P Cycles per Second

## Slide 42: Basic Performance Equation
T = (N x S)/R
T – processor time required to execute a program (program execution time)
N – machine language instructions
S – Average number of basic steps needed to execute one machine instruction
To achieve high performance
  Reduce the value of T
  Which means reducing N and S and increasing R

## Slide 43: Basic Performance Equation
N – is reduced if the source program is compiled into fewer machine instructions
S – is reduced if instructions have a smaller number of basic steps to perform or if the execution of instructions is overlapped
Using higher frequency of clock increases the value of R
  Means that the time required to complete a basic execution step is reduced

## Slide 44: Traditional Pipeline Concept
Laundry Example
Ann, Brian, Cathy, Dave each have one load of clothes to wash, dry, and fold
Washer takes 30 minutes
Dryer takes 40 minutes
“Folder” takes 20 minutes
A
B
C
D

## Slide 45: Traditional Pipeline Concept
Sequential laundry takes 6 hours for 4 loads
If they learned pipelining, how long would laundry take?
A
B
C
D
30
40
20
30
40
20
30
40
20
30
40
20
6 PM
7
8
9
10
11
Midnight
Time

## Slide 46: Traditional Pipeline Concept
Pipelined laundry takes 3.5 hours for 4 loads
A
B
C
D
6 PM
7
8
9
10
11
Midnight
T
a
s
k
O
r
d
e
r
Time
30
40
40
40
40
20

## Slide 47: Traditional Pipeline Concept
A
B
C
D
6 PM
7
8
9
T
a
s
k
O
r
d
e
r
Time
30
40
40
40
40
20

## Slide 48: Pipelining and Super Scalar Operation
Instructions are executed one after another
High performance – by overlapping the execution of successive instructions, using a technique called pipelining
Add R1, R2, R3; R3  R1+R2;
The processor can read the next instruction from memory while the addition operation is being performed
One instruction is completed in each clock cycle
S = 1; can not be attained in practice for variety of reasons
However, pipelining increases the rate of executing instructions significantly and causes the effective value of S  1

## Slide 49: Pipelining and Super Scalar Operations
Higher degree of concurrency can be achieved if multiple instruction pipelines are implemented in the processor
This means multiple functional units are used
Creating parallel paths through which different instructions can be executed in parallel
It is possible to execution of several instructions in every clock cycle
This mode of operation is called super scalar execution

## Slide 50: Clock Rate
Improving the Integrated Circuit (IC) technology makes logic circuits faster
Which reduces the time needed to complete a basic step
This allows clock period P to reduced and the clock rate to R to be increased
Reducing the amount of processing done in one basic step also makes it possible to reduce the clock period P

## Slide 51: Instruction Set: CISC and RISC
Simple instructions require a small number of basic steps to execute
Complex instructions involve a large number of steps
The processors that has only simple instructions
  A large number of instructions may be need to perform a given programming tasks
  This could lead to a large value of N and a small value of S

## Slide 52: Instruction Set: CISC and RISC
If individual instructions perform more complex operations
  Fewer instructions will be needed
  Leading to a lower value of N and a larger value of S
It is obvious if one choice is better than the other
A key consideration in comparing the two choices is the use of pipelining (S1)
Complex instructions combined with pipelining would achieve the best performance

## Slide 53: Compiler
Translates a high level language program into a sequence of machine instructions
To reduce N – A suitable machine instruction set and a compiler that makes good use of it
An optimizing compiler takes advantage of various features of the target processor to reduce the product NxS (total number clock cycles to execute)
The compiler may rearrange the program instructions to achieve better performance

## Slide 54: Performance Measurement
The time it takes a computer to execute a given benchmark (Program)
System Performance Evaluation Corporation (SPEC) develops benchmark programs for different application programs
The program selection range from
  Game playing
  Compiler
  Data base applications to numerically intensive programs astrophysics
  Quantum chemistry

## Slide 55: Performance Measurement
In each of the case program is compiled for computer under test and the running time on a real computer is measured
SPEC rating = (running time on the reference computer )/(running time on the computer under test

## Slide 56: Multiprocessors
Computer system that has more than one processors called Multiprocessors
These systems either execute a number of different application tasks in parallel
Or they execute subtasks of a single large task in parallel
All the processors usually have access to all of the memory in such systems – Shared memory multiprocessor systems
High performance of these systems comes with much increased complexity and cost
Cost is increased because of more complex interconnection networks

## Slide 57: Multi-Computers
It is also possible to use an interconnected group of complete computers to achieve high total computational power
The computers normally have access only to their own memory units
When the tasks they are executing need to communicate data, they do so by exchanging message over a communication network
Shared memory concepts of multi processor different the Message passing multi-computers

## Slide 58: Organization of a Computer
Dr Noor Mahammad Sk

## Slide 59: Organization of a Computers
Based on the connections between Data/program Memory and Processors
Two
  Von Neumann Architectures
  Harvard Architectures

## Slide 60: Van Neumann
The van Neumann architecture has only one memory space to store both program and data Memory
Fetches instructions and data from one memory
Limits Operating Bandwidth
  One piece of data or One instruction at a one time
CPU
Data
Instructions

## Slide 61: Harvard Architecture
There are two separate Memory spaces, one for instruction and one for data
Increased Through put
  While you are executing one instruction, you can be fetching the next instruction
  Different program and data bus width are possible
CPU
DATA
Instructions

## Slide 62: Reference
Computer Organization by Carl Hamacher, Zvonko Vranesic, Safwat Zaky, Mc Graw Hill Publications